## Slide 1
Research Report
Vo Khoi Thanh Son
3-5-2024

## Slide 2
Previous work
Observations: object_pose ( pos (3) and rot (4) )
 Not enough to locate good grasping points on complex objects
Reward shaping:
 Modify the reward for better grasping
Train the gripper to grasp different types of objects
 High success rate on small objects
Switch to bigger objects  Fail to grasp

## Slide 3: Object observations
Bounding box
Extract the oriented bounding box (OBB) from the object mesh
Calculate and update the bounding box of object
Initialize bounding box for the object
trimesh.bounds.oriented_bounds(mesh)
+ OBB represents a 3D box that is oriented to tightly fit around the given mesh object
+ OBB can be oriented arbitrarily in 3D space based on the object's geometry.
- OBB parameters:
+ Center.
+ Extents.
+ Position offset
+ Rotation offset
- During updates, compute:
+ Bbox Position
+ Bbox Rotation
 self.object_bbox_pose = torch.cat([bbox_pos, bbox_rot], dim=1)
+ Bbox Corners
 update Bbox Bounds

## Slide 4: Object observations
Surface sampling
Extract points on the object surface from the object mesh
Calculate and update the surface samples of object
Initialize surface sample offset positions for objects
trimesh.sample.sample_surface(object_mesh, count=20)
+ Generate points on each surface that represent the object’s geometry
+ Retrieves position of points sampled on the surface for the object identified
 Append points to a list containing surface sample offset positions for all envs.
During updates, reshape:
+ object pos
+ object rot
 self.object_surface_samples = object_pos + quat_apply ( object_rot, self.object_surface_sample_offset_pos)

## Slide 5: Reward shaping
Gripping reward
+ d: distance between gripper base and object
+ Opened gripper when approaching the object:
+ When d is minimized, close the gripper:

## Slide 6: Reward shaping
Contact reward
+ Reward for discouraging large distances between the fingertips and the object surface

## Slide 7: Gripper observations
Hardware conditioned policy
Pos: the fingers have difficulties holding the object
)
- Compute the relative pose between the joints
Kinematic:

## Slide 8: Gripper observations
+ Find inverse of quaternions of the joint
- Compute the relative orientation between the joints
+ Find rotation transformation by multiplying quat inverse of joint 1 with joint 2 quat
Kinematic:

## Slide 9: Gripper observations
- Construct the dynamics vector
- Extract the dynamics properties of gripper dofs
self.gripper_dyn = torch.cat([self.gripper_stiffness, self.gripper_damping, self.gripper_friction, self.gripper_armature], dim=-1)
stiffness | float32 | Drive stiffness.
damping | float32 | Drive damping.
friction | float32 | DOF friction.
armature | float32 | DOF armature.

## Slide 10: Future work
- Modifying the reward structure for better grasping, improve performance
- Implement hardware vector to train with different kinds of grippers and compare the success rates
- Test generalization with unseen objects and grippers

## Slide 11: Thanks!