## Slide 1: Research Goal
Journal Review
Visual Dexterity: In-Hand Reorientation of Novel and Complex Object Shapes
A real-time controller that dynamically reorients complex and new objects by any amount using a single depth camera
reorient objects into any orientation
generalize to new and complex objects
operate in real time using data from commodity sensors
Real world reorientation system

## Slide 2: Challenge
+ Real-world setup choices:
Placing multiple cameras around the workspace
Upwards facing hand configuration instead of downwards facing hand configuration

## Slide 3
+ Object reorientation problem:
High-dimensional control space
Measuring the state information the controller requires
Challenge
Touch sensors?

## Slide 4: Methods
Build a controller using deep reinforcement learning (RL)
How to train controllers with sensors available in the real world
sim-to-real transfer problem

## Slide 5: Training RL controllers from visual inputs
Inferring the relevant state information
Determining the optimal action
Two-stage teacher-student training paradigm
Teacher policy
Student policy

## Slide 6: Training RL controllers from visual inputs
trained via RL with priviliged state information
slow speed of rendering
Teacher policy
Student policy
Synthetic point cloud
Rendered point cloud
2-stage approach

## Slide 7: Overcoming the sim-to-real gap
- Differences in
motor/object dynamics
perception noise
modeling approximations
- Achieving precise control in a system with fast-changing dynamics
- Using a downward-facing hand configuration

## Slide 8: Experiment
Three-fingered D’Claw manipulator and a modified four-fingered version with 9 and 12 degrees of freedom (DoFs)
- Big dataset: 150 objects from internet sources
- Small dataset:
+ 7 objects for the training dataset
+ 5 objects for the testing dataset
Object datasets
5 table materials.

## Slide 9: Experiment
Downward-facing hand configuration with 2 settings:
With and without a supporting table

## Slide 10: Experiment
Real-world observations:
+ The joint positions of each motor in the robotic hand
+ The depth image from the RealSense camera
Observation space for teacher policy:
+ joint positions and velocities
+ fingertip pose and velocities
+ object pose and velocity
+ target orientation expressed as a quaternion
+ rotation difference between current and target object orientation
Training setup

## Slide 11: Results
Using a three-fingered manipulator with rigid and soft fingertips
+ rigid 3D-printed fingertips (row A)
+ soft elastomer fingertips (row B)
Object reorientation with a supporting surface

## Slide 12: Results
Different supporting materials
+ Tablecloth, an uneven door mat, a slippery acrylic sheet, and a perforated bath mat
Object reorientation with a supporting surface

## Slide 13: Results
Four-fingered robot hand operating without the need for a supporting surface
Object reorientation in air

## Slide 14: Practice
Simulating a 3-fingered gripper in Isaac Gym