## Slide 1
Research Report
Vo Khoi Thanh Son
16-7-2024

## Slide 2: Project Goal
- Implement RL algorithm to train soft grippers to grasp different objects and transfer to the real world environment.
- Train a single policy that can generalize to
different types of grippers
different object shapes
- 2-stage teacher-student paradigm
Teacher policy: privileged state information (gripper’s pose, gripper joints (dofs), object pose, object id
Student policy: imitate the teacher using visual inputs from the camera
Position control (DOF_MODE_POS)
Effort control (DOF_MODE_EFFORT)
Control gripper’s base
Control the action of opening and closing the fingers

## Slide 3
Learn to use wandb to plot the results
- Reward shaping :
+ Reward for minimizing distance between gripper and object
+ Reward for lifting the object
+ Reward for the object to reach the goal height
+ Reward for minimizing the deviation in the gripper's orientation
Learn to modify the rewards for best performance
Set up the environment for training task
Learn to use tensors to represent high-dimensional data
Learn to use Isaac gym API to implement the task

## Slide 4
Training different types of grippers
- Create a set of different robot grippers based on a given 3-fingered gripper urdf file in Isaac Gym
relative distance
relative orientation matrix
Hardware vector defined by relative pose of consecutive joints

## Slide 5: Franka Panda with soft gripper simulation
Operational Space Control for robot arm (OSC):
+ perform tasks in Cartesian space (end-effector's pose) instead of joint space (joint angles)
+ actions: desired end-effector pose  joint torques  gym.set_dof_actuation_force_tensor
 Extract joint positions and velocities
calculate mass matrix
compute eef inertia matrix from jacobian tensor
 transform Cartesian action to joint torques by PD-control

## Slide 6
IsaacGymEnvs config
Taochenshh config
Set up environment for training using the learning algorithms built in taochenshh work